9.	17/2606/FUL - Erection of 2 no. 2 bed 3 person wheelchair user flats, 4 no. 2 bed 4 person flats and associated car parking and landscaping at GARAGES REAR OF 22 – 28 ASHRIDGE DRIVE, SOUTH OXHEY, HERTFORDSHIRE, for Ms Cummings

(DCES)

| Parish: Watford Rural | Ward: South Oxhey |
| --- | --- |
| Expiry Statutory Period: 2/3/18 (Agreed Extension) | Officer: Claire Westwood |
| Recommendation: That Planning Permission be approved. |
| Reason for consideration by the Committee: The applicant is Three Rivers District Council. |

1.	Relevant Planning History

1.1	17/2076/FUL - Erection of 2 no. 2 bed 3 person wheelchair user flats, 6 no. 2 bed 4 person flats and associated car parking and landscaping.  Withdrawn.

2.	Site Description

2.1	The site is located off Ashridge Drive to the rear of properties in Ashridge Drive and Ellesborough Close.  The main part of the site is roughly rectangular in shape with a maximum width of approximately 35 metres (north west to south east) and maximum depth of approximately 30 metres (north east to south west).  The site is accessed via a single access drive from Ashridge Drive between No’s. 28 and 30 Ashridge Drive.  The site was occupied by 17 flat roofed garages, however, these have been demolished and the site is currently used to provide temporary storage for vehicles owned by a local car sales garage.

2.2	The access drive and north west flank site boundary run adjacent to the flank boundary of No. 30 Ashridge Drive, a two-storey semi-detached dwelling.  The north eastern site boundary adjoins a wooded area with Ashridge play area beyond.  There is an existing informal pedestrian access to the woodland.  The south east site boundary adjoins the rear garden boundaries of No’s 22 – 25 Ellesborough Close.  The south west site boundary adjoins the rear gardens of No. 26 Ellesborough Close and No’s 22 – 28 Ashridge Drive.

2.3	The area surrounding the application site is predominantly residential, characterised by a mixture of two-storey semi-detached and terraced properties.

3.	Description of Proposed Development

3.1	Planning permission is sought for the erection of 6 flats, comprising of 2 no. 2 bed 3 person wheelchair accessible flats and 4 no. 2 bed 4 person flats with associated car parking and landscaping.

3.2	The flats are intended to provide temporary residential accommodation.  The Affordable Housing Statement sets out that the accommodation is required in response to the District’s pressing need for emergency accommodation.  The application proposes a permanent structure to provide temporary/emergency accommodation for persons that are registered with the Local Authority as being homeless.

3.3	The flats would be provided in 3 blocks of rectangular footprint linked by stair cores and stepped across the site from north east to south west.  The building would be 2 storeys in height.  Each of the 3 blocks would have a depth of 12.4 metres and width of 6.4 metres.  The 2 stair cores would each have a maximum depth of 8.2 metres and maximum width of 2.6 metres.  The development would have a maximum width of approximately 24.8 metres.

3.4	The block to the north east (Block 1 for the purposes of this report) would be sited approximately 1 metre from the north east boundary with the wooded area, a minimum of 2.8 metres from the rear boundary of No. 22 Ellesborough Close and 12.6 metres from the boundary of No. 30 Ashridge Drive.

3.5	The central block (Block 2 for the purpose of this report) would be sited approximately 6 metres from the rear garden boundary of No. 24 Ellesborough Close and between 12 – 15 metres from the boundary of No. 30 Ashridge Drive.

3.6	The southern block (Block 3 for the purpose of this report) would be sited a minimum of 1 metre from the boundary with No’s. 24 – 28 Ashridge Drive, 8.4 metres from the rear boundary of properties in Ellesborough Close and between 12 – 14 metres from the boundary of No. 30 Ashridge Drive.

3.7	The development would include gable ends to both the front and rear elevations with a maximum ridge height of approximately 8 metres and an eaves height of 5.6 metres.  The central stair cores would have flat roofs at the eaves level.

3.8	Fenestration is proposed to the front and rear and elevations of all Blocks.  Flank glazing to Blocks 1 and 2 and is shown as obscure glazing on the south west flanks.  Flank glazing to Block 3 is restricted to the internal facing elevation.  Oriel (angled) windows are proposed within the rear elevations of all Blocks.  Grey roof tiles are proposed for the roof and as cladding to the upper floor levels, with a contrasting red brick to the ground floor.

3.9	The existing access would be retained to serve the development.  Eight car parking spaces are proposed (including 2 accessible spaces) to the front of the Blocks with cycle storage provided within the stair cores (6 spaces).  Refuse storage is proposed to the front of the Blocks and would comprise a 1.7 metre high natural timber enclosure.  An area of soft landscaping/amenity space would be provided to the rear of the Blocks.  The existing pedestrian access to the woodland would be retained.

3.10	In response to concerns raised, amended plans have been submitted during the application which propose the introduction of timber bollards to the perimeter of the grass verge to the front of No’s. 30 – 36 Ashridge Drive.  This is to ensure that the verge cannot be accessed by vehicles for parking.

3.11		The application is accompanied by:

- Biodiversity Survey and Report

- Design and Access Statement

- Land Contamination Assessment

- Phase 1 Desk Study Report

- Energy Report

- Affordable Housing Statement

- Transport Assessment

- Arboricultural Report

4.	Consultation

4.1	Statutory Consultation

4.1.1	National Grid: No comments received.

4.1.2	Landscape Officer: [No objection subject to conditions]

I have looked at the proposed development and have no significant objection to the proposed scheme, provided adequate provision is made for the protection of trees to be retained.

The trees adjacent to the garage site in Ashridge Drive are not the subject of a TPO and the site has no other designation. It is adjacent to Prestwick Road Meadows Local Nature Reserve which is on the other side of Prestwick Road to this site. The site is public open space and there is a play area sited to the SE of the site. The site is currently treed with several significant and mature Oak tree specimens, which are worthy of note. The site is significant to the amenity of the local area and so any loss of trees should be avoided if possible.

There is likely to be on-going pressure to prune trees within the adjacent Prestwick Road Meadows (North) site as the proposed development takes the building nearly up to the boundary.

T2 and T8 are both very mature Oaks and as such are of significant size compared to the proposed residential units. There is real concern that this may lead to future occupiers of these units being concerned about the risk that these trees pose. T2 is by far the most prominent of all trees on the site and as such should be protected from construction damage where possible. The tree report refers to T8 and talks about the possibility of it becoming a veteran tree. My concern is that a tree of this maturity may well be affected more significantly by the proposed development and as a result may fall rapidly into decline following the development of the site.

Part of the construction falls within the Root Protection Area of T8 and other smaller trees along the boundary. Trees affected include:

T9 	Ash	Removal	Not particularly significant to amenity.

T10	Oak 	Removal	It is unfortunate to lose this tree however I accept the reasons why this tree should be removed if the development is allowed as it would become a problem in such close proximity to a building.

T11	Retain	Wild Plum may impact on proposed development longer term.

T8	Retain	Oak 	(RPA encroached upon by building)

T2	Retain	Oak	(RPA significantly by hard-standing and access)

T12	Off site tree	Ash 	May impact on site through shading. This tree is privately owned however the report has already mentioned the potential of this tree to shade the proposed dwelling. This is likely to lead to further future pressure to cut this tree back in future.

Temporary Ground Protection during construction will assist in the reduction of any impact of development on the trees to be retained. It will however not prevent damage. T2 is probably the most significant tree on the site and over half of its Root Protection Area (RPA) is likely to be impacted upon by the proposed works (albeit not the building itself). I accept that there is already hard-standing in the area of the garage site, however to take this up and replace it with something else is potentially likely to have a significant impact. This work should be very carefully considered.

If we do decide to grant consent I would recommend the following conditions:

1.	Landscaping – Details – CR095

No development shall take place until there has been submitted to and approved in writing by the Local Planning Authority a scheme of hard and soft landscaping, which shall include the location of all existing trees and hedgerows affected by the proposed development, and details of those to be retained, together with a scheme detailing measures for their protection in the course of development.

All hard landscaping works required by the approved scheme shall be carried out and completed prior to the first occupation of the development hereby permitted. All soft landscaping works required by the approved scheme shall be carried out in accordance with a programme to be agreed before development commences and shall be maintained including the replacement of any trees or plants which die are removed or become seriously damaged or diseased in the next planting season with others of a similar size or species, unless the Local Planning Authority gives written consent to any variation for a period for five years from the date of the approved scheme was completed.

Reason: In the interests of visual amenity in accordance with Policies CP1 and CP12 of the Core Strategy (adopted October 2011) and Policy DM6 of the Development Management Policies LDD (adopted July 2013).

2.	Tree Protection Scheme- Details – CR098

No operations (including tree felling, pruning, demolition works, soil moving, temporary access construction, or any other operation involving the use of motorised vehicles or construction machinery) shall commence on site in connection with the development hereby approved until the branch structure and trunks of all trees shown to be retained and all other trees not indicated as to be removed and their root systems have been protected from any damage during site works, in accordance with a scheme to be submitted to and approved in writing by the Local Planning Authority.

The protective measures, including fencing, shall be undertaken in accordance with the approved scheme before any equipment, machinery or materials are brought on to the site for the purposes of development, and shall be maintained until all equipment, machinery and surplus materials have been removed from the site.  Nothing shall be stored or placed within any area fenced in accordance with this condition and the ground levels within those areas shall not be altered, nor shall any excavation be made, without the written consent of the Local Planning Authority. No fires shall be lit or liquids disposed of within 10.0m of an area designated as being fenced off or otherwise protected in the approved scheme.

Reason: To protect the visual amenities of the trees, area and to meet the requirements of Policies CP1 and CP12 of the Core Strategy (adopted October 2011) and Policy DM6 of the Development Management Policies LDD (adopted July 2013).

3.	Arboricultural Method Statement – CR100A

No development or other operation shall commence on site until a scheme (herein called the Approved Method Statement of Arboricultural Works Scheme) which indicates the construction methods to be used in order to ensure the retention and protection of tree, shrubs and hedges growing on or adjacent to the site has been submitted to and approved in writing by the local planning authority.

No operations shall commence on site in connection with the development hereby approved (including tree felling, pruning, demolition works, soil moving, temporary access construction, or any other operation involving the use of motorised vehicles or construction machinery) until the tree protection works required by the approved scheme are in place on site.

The fencing or other works which are part of the approved scheme shall not be moved or removed, temporarily or otherwise, until all works including external works have been completed and all equipment, machinery and surplus materials removed from the site, unless the prior approval of the local planning authority has first been sought and obtained.

Reason: To ensure that the protected trees are not affected during construction of the development hereby permitted, in the interests of visual amenity and in accordance with Policies CP1 and CP12 of the Core Strategy (adopted October 2011) and Policy DM6 of the Development Management Policies LDD (adopted July 2013).

I would not expect a significant tree planting scheme as part of the development, however the proposals should include an element of soft landscaping.

4.1.3	Hertfordshire Ecology: [No objection]

Thank you for consulting Hertfordshire Ecology on this application. I note we have previously commented on proposals at this address (Anita Parry, 13/11/2017), and I reiterate those comments here:

The Hertfordshire Environmental Records Centre does not have any habitat or species records for the application site, which is an area of hardstanding tarmac with garages and bordering trees and scrub. To the north is the woody part of “Prestwick Road Meadows, North”.

The site is of limited ecological interest. However, there is some potential for nesting birds to use the trees and scrub on and adjacent to the site. Bats may also be using the adjacent woodland for foraging and commuting.

I advise the following Informatives are added to any permission granted:

“The removal or severe pruning of trees and shrubs should be avoided during the bird breeding season (March to August inclusive [Natural England]) to protect breeding birds, their nests, eggs and young. If this is not practicable, a search of the area should be made no more than 3 days in advance of vegetation clearance and if active nests are found, the location should be cordoned off (minimum 5m buffer) until the end of the nesting season and/or works should stop until the birds have left the nest.”

“Any external lighting scheme should be designed to minimise light spill, in particular directing light away from the boundary vegetation to ensure dark corridors remain for use by wildlife as well as directing lighting away from potential roost / nesting sites.”

I welcome the ecological enhancements suggested in the Ecology Report and hope these are incorporated within the development scheme.

4.1.4	Hertfordshire Highways: [No objection subject to conditions]

Notice is given under article 18 of the Town and Country Planning (Development Management Procedure) (England) Order 2015 that the Hertfordshire County Council as Highway Authority does not wish to restrict the grant of permission subject to the following conditions:

Conditions:

- Prior to the commencement of the development hereby permitted full details (in the form of scaled plans) shall be submitted in relation to the proposed parking / access area to demonstrate the following:

- Swept Path analysis for vehicles using the site.

Reason: In the interest of highway safety and traffic movement.

- The development shall not begin until full details of all proposed construction vehicle access, movements, parking arrangements and wheel washing facilities have been submitted to and approved in writing by the Local Planning Authority. The relevant details should be submitted in the form of a Construction Management Plan and the approved details are to be implemented throughout the construction programme.

Reason: To minimise danger, obstruction and inconvenience to users of the highway in accordance with Policies CP1 and CP10 of the Core Strategy (adopted October 2011) and Policy DM13 and Appendix 5 of the Development Management Policies LDD (adopted July 2013).

Highway Informative:

HCC recommends inclusion of the following highway informative / advisory note (AN) to ensure that any works within the public highway are carried out in accordance with the provisions of the Highway Act 1980:

AN) Storage of materials: The applicant is advised that the storage of materials associated with the construction of this development should be provided within the site on land which is not public highway, and the use of such areas must not interfere with the public highway. If this is not possible, authorisation should be sought from the Highway Authority before construction works commence. Further information is available via the website

https://www.hertfordshire.gov.uk/services/highways-roads-and-pavements/highways-roads-and-pavements.aspx or by telephoning 0300 1234047.

Comments/Analysis:

The proposal comprises of the development of six two-bed flats and associated car parking at a garage site at Ashridge Drive, South Oxhey.  Ashridge Drive is designated as an unclassified local access road, subject to a speed limit of 30mph and highway maintainable at public expense.

Vehicle Access and Parking:

The site is accessed via a 28m long private access road that runs between 28 and 30 Ashridge Drive. The access road is approximately 4m wide at its narrowest point encompassing a circa 3.2m wide carriageway. This carriageway then varies between circa 3.5m to 4.8m along the remainder of its length. The current vehicular and pedestrian visibility at the junction with Ashridge Road is considered to be acceptable and in accordance with Manual for Streets (MfS) and Roads in Hertfordshire: A Design Guide.

The proposal includes the provision of eight on site car parking spaces, two of which are disabled spaces. The layout is shown on submitted plan no. 020A.  HCC as Highway Authority considers that the dimensions of the proposed parking spaces are acceptable and in accordance with MfS and Roads in Hertfordshire.   However HCC is requesting further information in the form of swept path analysis to demonstrate that cars parking on site would be able to safely manoeuvre and not cause a conflict between different users.

The level of parking is not in accordance with car parking standards as outlined in Appendix 5 of Development Management Policies: Local Development Document and there will be a loss of garage use for surrounding properties. However it is unlikely that any effects from parking would be significant enough to recommend refusal from a highway perspective. TRDC is the parking authority for the district and therefore should ultimately be satisfied with the parking provision.

Refuse/Waste Collection:

Provision has been made for on-site bin/refuse storage as shown on submitted plan no. 400.  Provision should be made for an on-site bin-refuse store within 30m of the dwelling and within 25m of the kerbside/bin collection point, which has been achieved. Waste collection would presumably be from Ashridge Drive.

Emergency Vehicle Access:

The proposed access road varies from between circa 3.2m to 4.5m. Although less than the recommended 3.7m wide at its narrowest point, the arrangements would enable fire trucks to get to within 45m to all parts of the proposed dwellings and not have to reverse more than 25m out of the site. This is in accordance with the guidance in MfS, Roads in Hertfordshire; A Design Guide and Building Regulations 2010: Fire Safety Approved Document B Vol 1 - Dwellinghouses.

Conclusion:

HCC as Highway Authority has considered that the proposal would not have an unreasonable or significant impact on the safety and operation of the surrounding highway with no direct impact. The development is unlikely to result in a material increase in traffic generation. HCC has no objections on highway grounds to the application, subject to the inclusion of the above planning conditions and informative.

4.1.5	Herts Constabulary: No comments received.

4.1.6(a)	Housing Officer: [Support]

We currently have 65 homeless families in temporary accommodation. Of these 65 homeless cases 26 are currently placed in temporary accommodation out of our district with the furthest away being in Harlow, Essex. This clearly demonstrates that temporary accommodation within the district is greatly needed for homeless families.

I support this application based on our temporary housing needs.

4.1.6(b)	Further comments:

There has been a change in figures since I commented on this application. We currently have 53 families in temporary accommodation. Of these we have 11 families in temporary accommodation out of the district.

4.1.7	Watford Rural Parish Council: No comments received.

4.2	Public Consultation

4.2.1	Number consulted:	 84	No responses received: 2

4.2.2	Site Notice: Expired 11/01/18	Press Notice: Expired 26/01/18

4.2.3	Summary of Responses

    - Overdevelopment;

    - Adverse effect on Conservation Area;

    - Loss of light/Overshadowing;

    - Proximity to neighbouring dwellings;

    - Impact on fence;

    - Overlooking and loss of privacy;

    - Impact on views and outlook;

    - Additional traffic;

    - Insufficient parking;

    - Negative impact on property value.

4.2.4	Officer comment: Material planning considerations are addressed in analysis below.  The application site is not within or adjacent to a Conservation Area.  Impact on property value is not a material planning consideration.

5.	Reason for Delay

5.1	No delay.

6.	Relevant Planning Policy, Guidance and Legislation

6.1	The Three Rivers Local Plan

The Core Strategy was adopted on 17 October 2011 having been through a full public participation process and Examination in Public. Relevant policies include Policies PSP2, CP1, CP2, CP3, CP4, CP6, CP8, CP9, CP10 and CP12.

The Development Management Policies Local Development Document (LDD) was adopted on 26 July 2013 after the Inspector concluded that it was sound following Examination in Public which took place in March 2013. Relevant policies include DM1, DM4, DM6, DM8, DM9, DM10, DM11, DM12, DM13 and Appendices 2 and 5.

The Site Allocations LDD was adopted in November 2014 having been through a full public participation process and Examination in Public.

The Community Infrastructure Levy (CIL) Charging Schedule (adopted February 2015).

6.2	National Planning Policy Framework (NPPF)

On 27 March 2012, the framework of government guidance in the form of Planning Policy Statements and Planning Policy Guidance Notes was replaced by the National Planning Policy Framework (NPPF). The application has been considered against the policies of the Core Strategy (adopted October 2011), the Development Management Policies Local Development Document (adopted July 2013) and the Site Allocations Local Development Document (adopted November 2014) as well as government guidance. The policies of Three Rivers District Council reflect the content of the NPPF.

6.3	Other

The Localism Act received Royal Assent on 15 November 2011. The growth and Infrastructure Act achieved Royal Assent on 25 April 2013.

The Wildlife and Countryside Act 1981 (as amended), the Conservation of Habitats and Species Regulations 2010, the Natural Environment and Rural Communities Act 2006 and the Habitat Regulations 1994 may also be relevant.

Hertfordshire County Council Waste Core Strategy and Development Management Policies Development Plan Document (2012).  Policy 12 is relevant.

7.	Planning Analysis

7.1	Principle of Development

7.1.1	The proposal is to provide 6 units for temporary residential accommodation to address homelessness need in Three Rivers.

7.1.2	The application site is not identified as a housing site by the Site Allocations LDD (adopted 2014) and as such it is not currently identified as part of the District’s housing supply.  The site should therefore be considered a windfall site.

7.1.3	Policy CP2 of the Core Strategy (adopted October 2011) states that applications for windfall sites will be considered on a case by case basis having regard to;

- the location of the proposed development, taking into account the Spatial Strategy;

- the sustainability of the development and its contribution to meeting local housing needs;

- infrastructure requirements and the impact on the delivery of allocated housing sites; and

- monitoring information relating to housing supply and the Three Rivers housing target.

7.1.4	The Spatial Strategy identifies South Oxhey as a Key Centre and comments that new development will be directed towards previously developed land and appropriate infilling opportunities within the Principal Town and Key Centres as these have been identified as the most sustainable locations in the District.

7.1.5	The Core Strategy sets out the long term Spatial Vision for Three Rivers and the strategic policy objectives required to deliver that vision.  Spatial Vision priority (c) is; ‘to improve access to housing and affordable housing for communities across the whole District’.

7.1.6	Strategic Objective S4 within the Core Strategy (adopted October 2011) seeks to balance the community’s need for future homes by providing sufficient land to meet a range of local housing needs.

7.1.7	Policy CP1 (Overarching Policy on Sustainable Development) of the Core Strategy (adopted October 2011) advises that all development in Three Rivers will contribute to the sustainability of the District.  This means taking into account the need to:

d) Make efficient use of land by guiding development onto previously developed, brownfield land…

7.1.8	Policy CP3 (Housing Mix and Density) requires that proposals take into account the range of housing needs in terms of size and type of dwellings.  This includes provision of specialist accommodation.  Policy CP4 relates to affordable housing provision.

7.1.9	It is recognised that there is a significant need for temporary residential accommodation within the District.  The Council provides on average between 60-90 units of temporary accommodation for homeless households with a number of people having to be housed outside of the District. Whilst not an identified housing site, the site is previously developed and within a Key Centre and considered to be in a sustainable location.  In accordance with Policy CP3, the proposal helps meet the future needs of the District’s homeless population and provides the housing type most suited to their needs.  As such, there is no objection in principle to the nature of the development proposed subject to compliance with other relevant planning policies.

7.1.10	Policy CP4 of the Core Strategy (adopted October 2011) requires that all new development resulting in the net gain of one or more dwellings will be expected to contribute to the provision of affordable housing.  As the development would provide housing for homelessness need it would provide 100% affordable housing.  A condition on any grant of consent would require that the accommodation is only occupied by persons that are registered with the Local Authority as being homeless.

7.1.11	The site was previously occupied by 17 garages, however, the garages have been demolished and the site is therefore not currently used by local residents for parking.

7.2	Character/Street Scene/Design

7.2.1	Policy CP1 of the Core Strategy (adopted October 2011) seeks to promote buildings of a high enduring design quality that respect local distinctiveness and Policy CP12 of the Core Strategy (adopted October 2011) relates to design and states that in seeking a high standard of design the Council will expect development proposals to 'have regard to the local context and conserve or enhance the character, amenities and quality of an area'.  Development should make efficient use of land but should also respect the 'distinctiveness of the surrounding area in terms of density, character, layout and spacing, amenity, scale, height, massing and use of materials'; 'have regard to the local context and conserve or enhance the character, amenities and quality of an area' and 'incorporate visually attractive frontages to adjoining streets and public spaces'.

7.2.2	In terms of new residential development, Policy DM1 of the Development Management Policies LDD (adopted July 2013) advises that the Council will protect the character and residential amenity of existing areas of housing from forms of ‘backland’, ‘infill’ or other forms of new residential development which are inappropriate for the area.  Development will be only be supported where it can be demonstrated that the proposal will not result in:

- Tandem development;

- Servicing by an awkward access drive which cannot easily be used by service vehicles;

- The generation of excessive levels of traffic;

- Loss of residential amenity;

- Layouts unable to maintain the particular character of the area in the vicinity of the application site in terms of plot size, plot depth, building footprint, plot frontage width, frontage building line, height, gaps between buildings and streetscape features (e.g. hedges, walls, grass verges etc.)

7.2.3	The proposed development would not result in a tandem development.  The site would be served by an existing access, highways matters are discussed below, however, it is noted that the Highway Authority consider the access to be acceptable and raise no objections.  Similarly, the introduction of 6 units is not considered to generate excessive levels of traffic.  Residential amenity is discussed in full below.

7.2.4	The proposed development would be sited on a former garage site surrounded by two-storey residential development to the north, west and south with a wooded area to the east.  The proposal would therefore result in a backland development which Policy DM1 of the Development Management Policies LDD (adopted July 2013) details will only be supported where it would not result in a layout unable to maintain the particular character of the area.

7.2.5	In terms of layout, the development would be served by an existing access creating a small no-through road off Ashridge Drive.  Dwellings fronting Ashridge Drive follow a linear form, although the building line varies due to the bend in the road.  There are existing no-through roads in the immediate vicinity include Ellesborough Close immediately to the south of the site and opposite.  It is not therefore considered that a layout introducing a development to the rear of existing dwellings would be out of character when considering the existing pattern of development.

7.2.6	Built form in the immediate vicinity is of a two-storey nature.  Whilst of a traditional design there is a mixture of hipped and gabled roof forms and also variation in materials.  The proposed development would be two-storeys and would therefore reflect that existing.  The indicative site elevations submitted with the application indicate that the ridge height would be lower than those of adjacent dwellings.

7.2.7	The proposed development would introduce flats in an area predominantly characterised by single family dwellings, however, there are existing flats including maisonettes immediately to the south of the site on Ellesborough Close.  The principle of flatted development is therefore not out of character with the area and it is not considered that the introduction of flats within the site would result in any material harm to the character of this residential area. Furthermore, the use of the buildings as flats would not be readily apparent from public vantage points.

7.2.8	The proposed buildings would reflect the general design principles of the surrounding neighbouring buildings in that they would contain pitched roofs with gabled end features.  The buildings with their asymmetrical roof forms and oriel windows would introduce design features that would appear different to that of the existing neighbouring properties.  However, the introduction of a building which does not reflect the design of existing built form does not automatically mean the proposal would result in harm to the character and appearance of the area or street scene.  The NPPF advises (para 60) that; “Planning policies and decisions should not attempt to impose architectural styles or particular tastes…”

7.2.9	The design features of the proposed buildings would introduce a sense of variation within the area which would not have a negative impact.  Furthermore, due to the siting of the development the views from public vantage points would be limited and where there would be views through it is not considered that the proposed buildings would appear prominent or obtrusive.

7.2.10	The height of the proposed buildings would not appear disproportionate in scale to that of the surrounding built form with the indicative site elevations showing the ridges set down from those of neighbouring dwellings. Whilst the development would increase the level of built form within the site, it would also introduce soft landscaping and it is not considered that the overall size and scale of the scheme would appear cramped or have an adverse impact on the character of the area.  Spacing would be maintained around the building within the site with additional spacing provided due to the separation distances to neighbouring dwellings (discussed in relation to residential amenity below).  It is considered that sufficient spacing would be maintained between the proposed buildings and neighbouring buildings as to prevent a cramped feature and the overall size, scale and footprint of the buildings would not result in overdevelopment or appear out of character.

7.2.11	Guidance in Appendix 2 of the Development Management Policies LDD (adopted July 2013) advises that development should be set in from flank boundaries at first floor level by 1.2 metres to ensure appropriate spacing and prevent a terracing effect.  In high density areas a minimum of 1 metre will be considered.  Both the northern and southern blocks would be sited a minimum of 1 metre from the respective boundaries.  This would accord with the 1 metre minimum in high density areas and it also noted that the intention of the guidance is to maintain spacing and prevent a terracing effect.  Due to the siting of the development to the rear of existing development it would not result in a terracing effect.

7.2.12	The footprint of the building would be staggered across the site with the 3 blocks set back from one another.  This would serve to break up the mass and bulk of the development.

7.2.13	There would be limited views of the proposed development from public vantage points along Ashridge Drive and Ellesborough Close through gaps between the existing built form and along the access road.  Due to the siting of the buildings and their set back from the surrounding highways they would not result in an unduly prominent feature.  There would also be views from the woodland to the east, although these would be restricted by the existing vegetation such that the development would not be prominent.

7.2.14	Materials proposed include red bricks (ground floor) and grey tile hanging (first floor) to the elevations with grey tiles to the roof which would match the tile hanging at first floor level.  Samples and details of all external materials would be required to be submitted by condition.

7.2.15	In summary, the proposed development would make efficient use of previously developed land and subject to conditions would not appear significantly out of character with the area in the vicinity of the application site.  The development would not appear unduly prominent in the street scene or result in adverse impacts on the character or appearance of the area. The proposal would therefore be acceptable in this regard in accordance with Policies CP1 and CP12 of the Core Strategy (adopted October 2011) and Policy DM1 and Appendix 2 of the Development Management Policies LDD (adopted July 2013).

7.3	Residential Amenity

7.3.1	One of the core planning principles listed in the NPPF (paragraph 17) is that planning should;

“Always seek to secure high quality design and a good standard of amenity for all existing and future occupiers of land and buildings”.

7.3.2	Policy CP12 of the Core Strategy (adopted October 2011) states that the Council will expect development proposals to;

c) Protect residential amenities by taking into account the need for adequate levels and disposition of privacy, prospect, amenity and garden space.

7.3.3	Design guidelines for residential development are set out in Appendix 2 of the Development Management Policies LDD (adopted July 2013).  New development should take into consideration impacts on neighbouring properties, both within and surrounding the development.  Distances between buildings should be sufficient so as to prevent overlooking, particularly from upper floors.  As an indicative figure, 28 metres should be achieved between the faces of single or two storey buildings backing onto each other.  Mitigating circumstances such as careful layout and orientation, screening and window positions may allow a reduction of distances between elevations.

Amenity of Neighbouring Occupiers:

7.3.4	The front elevation of the blocks would face towards the flank boundary of No. 30 Ashridge Drive.  No. 30 is set off the boundary with a detached garage in the space between.  The relative orientation is such that there would not be a back to back or facing relationship and the rear corner of No. 30 would be approximately 18.6 metres from the front of the closest block (Block C).  Although the proposed development would be readily visible from the rear elevations and gardens of the neighbouring properties to the north, the separation between the buildings and intervening access road and parking area, would provide an acceptable distance to prevent the proposal from resulting in a dominant or oppressive relationship to these neighbours.  First floor windows are proposed to the front elevation and would face towards the flank boundary of No. 30.  Whilst there would be views towards the neighbouring garden, views into the dwelling would be restricted to the relative orientation of the buildings and views of neighbouring gardens are not uncommon and form part of the existing relationship between buildings.

7.3.5	Block C would be orientated with its flank elevating facing towards properties in Ashridge Drive.  The front corner of Block C would be sited a minimum of 14 metres from No. 28 Ashridge Drive increasing to a distance of approximately 19.8 metres between the rear corner and No. 24 Ashridge Drive.  These existing dwellings are favourably sited to the south of the application site and the separation is such that it is not considered that the proposed development would result in overshadowing or loss of light.  No flank openings are proposed to Block C facing Ashridge Drive and as such there would be no overlooking of existing dwellings.  Blocks B and A would be visible to some existing dwellings in Ashridge Drive due to the stepped footprint.  A flank window is proposed in both Blocks A and B facing towards Ashridge Drive.  The closest (Block B) would be over 30 metres from properties in Ashridge Drive, however, given that in both cases the windows are secondary windows to the rooms that they serve, it would not be inappropriate to require the first floor flank windows to be obscure glazed and top opening only.  It is noted that this is shown on the submitted plans.

7.3.6	The rear elevation would face towards the rear of No’s. 22 – 25 Ellesborough Close, with No’s. 22 and 23 Ellesborough Close sited closest to the site boundary.  Block A would be sited a minimum of 19.2 metres from the rear of No. 22 and Block B would be sited approximately 17 metres from the rear of No. 23.  The distances are such that it is not considered that the development would result in overshadowing or loss of light.  The separation distance would not achieve the indicative 28 metre figure referenced in Appendix 2 in the interest of privacy, however, these guidelines do also state that mitigating circumstances such as careful layout and orientation, screening and window positions may allow a reduction of distances between elevations.  The proposed building would be angled away from the rear elevation of dwellings in Ellesborough Close and the plans also include Oriel windows at first floor level in order that any outlook from the proposed first floor units is directed towards the woodland to the north and not towards the rear of neighbouring dwellings.

7.3.7	The 3 blocks would be linked by 2 stair wells, full height angles louvres will protect neighbouring properties from overlooking whilst still allowing light into the cores.

7.3.8	The proposal would introduce 6 units on a former garage site.  Policy DM9 of the Development Management Policies LDD (adopted July 2013) details that the Council will ensure that noise from proposed commercial, industrial, recreational or transport use does not cause any significant increase in background noise level of near-by existing noise-sensitive property such as dwellings.  The use of the site for residential purposes would be compatible to that of the neighbouring properties and it is not considered that the change of use from garages to residential for 6 flats would result in any unacceptable noise and disturbance to neighbouring properties.  Similarly, given that the site was lawfully a garage site (17 garages) the proposal is unlikely to result in any increase in traffic noise from that of which could be generated by the previous use.  The use of the amenity space provision provided would be compatible to the residential gardens that surround the site and would not generate unacceptable levels of noise and disturbance.

Future Occupants

7.3.9	It is considered that sufficient privacy and natural light would be achieved to serve the proposed development.  Each unit would be served by a separate access from within the central stair cores.  Pedestrian access into the stair cores would be restricted and secured by the provision of full height screens with lockable gates.

Amenity Space:

7.3.10	Amenity space standards are set out in Appendix 2 of the Development Management Policies LDD (adopted July 2013).  There requirement for 2 bed flats is 31 square metres.  This would result in a requirement for 186 square metres to serve the development.

7.3.11	A small soft landscaped area would be located to the rear of the building, providing communal amenity space.  This would have a total area of approximately 170 square metres.  It is noted that provision would fall slightly short of the standard, however, it is noted that the site is within short walking distance of public open spaces such that it is not considered that the shortfall would result in such harm to amenity to justify the refusal of planning permission.

7.4	Highways & Access

7.4.1	Policy CP1 of the Core Strategy (adopted October 2011) advises that in ensuring all development contributes to the sustainability of the District, it is necessary to take into account the need to reduce the need to travel by locating development in accessible locations and promoting a range of sustainable transport modes.

7.4.2	Policy CP10 (Transport and Travel) of the Core Strategy (adopted October 2011) advises that all development should be designed and located to minimise the impacts of travel by motor vehicle on the District.

7.4.3	Hertfordshire Highways have reviewed the submitted details and raise no objections subject to conditions.

7.4.4	The site is accessed from Ashridge Drive, an unclassified local road subject to a 30mph speed limit.  There is an approximately 28 metre long private access drive that is sited between No’s. 28 and 30 Ashridge Drive.  The access is approximately 4 metres wide at its narrowest point at the entrance to the site but increases in width towards the rear.  The carriageway within that access ranges in width from 3.2 metres to 4.8 metres.  Due to the public footway along Ashridge Drive and the wide verge to the front of properties to the north, the current pedestrian and vehicular visibility at the junction with Ashridge Road is good and the Highways Officer comments that this is acceptable and in accordance with Manual for Streets (MfS) and Roads in Hertfordshire: A Design Guide.

7.4.5	The proposal includes 8 car parking spaces of which 2 would be disabled, to serve the 6 units.  The Highways Officer considers that the dimensions of the parking spaces is acceptable and in accordance with MfS, however, they have requested by condition further information in the form of swept path assessments to demonstrate that cars parking on site would be able to safely manoeuvre and not cause a conflict between different users.

7.4.6	In relation to refuse storage/collection (discussed below in more detail) no objection is raised as provision has been made within 30 metres of the dwellings and 25 metres of the collection point.

7.4.7	The access road varies in width from approximately 3.2 metres to 4.5 metres.  The Highways Officer notes that whilst this would in part be less than the recommended 3.7 metres, the arrangements would enable fire trucks to get to within 45 metres of all parts of the proposed dwellings and they would not have to reverse more than 25 metres out of the site. This is in accordance with the guidance in MfS.

7.4.8	There is an existing informal pedestrian access from the site into the woodland to the north, this is proposed to be retained.

7.4.9	In summary, the Highway Authority considers that the proposal would not have an unreasonable or significant impact on the safety and operation of the surrounding highway with no direct impact.  The development is unlikely to result in a material increase in traffic generation.  The Highway Authority therefore has no objections on highway grounds to the application subject to conditions and the proposal would be acceptable in this regard in accordance with Policies CP1, CP10 and CP12 of the Core Strategy (adopted October 2011).

7.5	Parking

7.5.1	The NPPF (paragraph 39) advises that, if setting local parking standards for residential and non-residential development, local planning authorities should take into account:

- The accessibility of the development;

- The type, mix and use of development;

- The availability of and opportunities for public transport;

- Local car ownership levels; and

- An overall need to reduce the use of high-emission vehicles.

7.5.2	The proposal relates to the provision of 6 units to provide temporary residential accommodation. Each unit would be self-contained with its own kitchen/dining/sleeping/bathroom facilities.  The submitted layout plans indicate that the development would provide 6 x 2 bed flats.

7.5.3	The application proposes 8 parking spaces.  Due to the layout and type of units proposed the parking requirements would be considered under Class C3 residential.

7.5.4	Parking standards are set out in Appendix 5 of the Development Management Policies LDD (adopted July 2013).  Appendix 5 also advises that the standards for car parking (except C3 Residential) may be adjusted according to which zone the proposed development is located in.   For two bedroom flats Appendix 5 of the Development Management Policies LDD stipulates that 2 spaces should be provided per unit.  This would result in a requirement for 12 spaces, resulting in a shortfall of 4 spaces against standards.

7.5.5	A Statement has been submitted with the application which provides details of the existing (as of 23.11.17) level of car ownership of households in temporary accommodation.  This shows that of 62 households in temporary accommodation only 55% (34) of the households have access to a car or cars.  Out of the 34 households with access to private transport only 4 (12% of the households with access to cars or a total of 6% of the households in temporary accommodation) of these households have access to two cars.  Put another way, of the total households in temporary accommodation (at 23.11.17):

- 4 households (6%) have use of two cars

- 30 households (48%) have use of one car

- 28 households (45%) do not drive or do not have access to a car

7.5.6	Parking allocation and management will be undertaken by the Housing Officer responsible for managing the scheme and the long term management of the parking areas and allocation details would be secured by condition.

7.5.7	Whilst the Highways Officer has requested swept path assessments by way of condition, they have commented that the parking spaces are of an appropriate size and whilst they note that there would be a shortfall against standards they do not consider that the effects from parking would be significant to justify refusal of planning permission.

7.5.8	The 2 ground floor flats are proposed to be wheelchair accessible.  Appendix 5 indicates that an accessible space should be provided for every home built to mobility standards.  The plans indicate 2 accessible spaces which would accord with standards.

7.5.9	In summary, taking into consideration the identified lower levels of car ownership of the residents who would occupy the buildings the provision of 8 parking spaces would be considered acceptable.  As the provision of parking would be on-site it is not considered that the proposed development would result in any greater impact on the existing parking pressures within the surrounding road networks.

7.5.10	In response to concerns raised, amended plans have been submitted during the application which propose the introduction of timber bollards to the perimeter of the grass verge to the front of No’s. 30 – 36 Ashridge Drive.  This is to ensure that the verge cannot be accessed by vehicles for parking.  Their implementation would be secured via condition.

7.5.11	Cycle parking standards are also set out in Appendix 5 and require (for flats) 1 space per 2 units.  This would result in a requirement for 3 cycle spaces.  Parking for 6 cycles is proposed, equating to 1 space per unit which would exceed standards.

7.6	Trees & Landscape

7.6.1	In ensuring that all development contributes to the sustainability of the District, Policy CP12 of the Core Strategy (adopted October 2011) advises that development proposals should:

i) Ensure that development is adequately landscaped and is designed to retain, enhance or improve important existing natural features; landscaping should reflect the surrounding landscape of the area and where appropriate integrate with adjoining networks of green open spaces.

7.6.2	The site is currently laid to hard standing.  There is a mature Oak (T2) adjacent to the western boundary and the northern site boundary adjoins a heavily treed area (Prestwick Road Meadows) with the canopies of some trees overhanging the application site.  Whilst these trees are not subject to a Tree Preservation Order, the Landscape Officer considers them to contribute to the amenity of the local area and notes that there are several significant and mature Oak trees.

7.6.3	The Landscape Officer has reviewed the submitted details which include an Arboricultural Report, and raises no objections provided that adequate provision is made for the protection of those trees which are to be retained.

7.6.4	T2 and T8 are mature Oak trees and the Landscape Officer has raised some concern that this may lead to future occupiers being concerned regarding the perceived risk these trees pose.  However, they are healthy trees and subject to appropriate management it is not considered that there would be actual harm.  T2 is proposed to be retained within the site and the submitted details indicate that this would be protected during construction, a condition on any grant of consent would require full details of proposed tree protection measures.

7.6.5	It is noted that part of the construction would fall within the Root Protection Area of T2, T8, T9, T10, T11 and T12.  T2, T8 and T11 are proposed to be retained and would need to be appropriately protected during construction. T9 (Ash) is proposed to be removed, however, this is not of amenity value and therefore no objection is raised.  T10 (Oak) is also proposed to be removed.  Whilst the Landscape Officer comments that its loss is unfortunate, they recognise the reasons why the removal is necessary and raise no objection.

7.6.6	The Landscape Officer has comments that temporary ground protection during construction will assist in the reduction of any impact of development on the trees to be retained.

7.6.7		In summary, subject to conditions relating to protective fencing and an arboricultural method statement, the Landscape Officer raises no objection to the proposed development.  A condition regarding the submission of details of landscaping would also be appropriate.  Whilst the Landscape Officer has clarified that a significant tree planting scheme would not be required, the proposals should include an element of soft landscaping.

7.7	Flood Risk & Drainage

7.7.1	The scale of the development is such that there is no statutory requirement for a Sustainable Drainage Scheme (SuDS) to be submitted.  Similarly, the site is located within Flood Zone 1 and as such a Flood Risk Assessment is not required to be submitted.  Policy DM8 of the Development Management Policies document stipulates that development will only be permitted where it would not be subject to unacceptable risk of flooding and would not unacceptably exacerbate risk of flooding elsewhere.  Where practicable existing flood risks should be reduced.

7.7.2	The existing site contains large areas of hard standing following the demolition of the pre-existing garages.  The proposal would introduce buildings with drainage provision and soft landscaping would also be introduced to the site.  As such it is considered that drainage would be improved and the development would not therefore result in any greater risk of flooding within the site or neighbouring properties.

7.8	Wildlife & Biodiversity

7.8.1	Section 40 of the Natural Environment and Rural Communities Act 2006 requires Local Planning Authorities to have regard to the purpose of conserving biodiversity. This is further emphasised by regulation 3(4) of the Habitat Regulations 1994 which state that Councils must have regard to the strict protection for certain species  required by the EC Habitats Directive.

7.8.2	The protection of biodiversity and protected species is a material planning consideration in the assessment of applications in accordance with Policy CP9 of the Core Strategy (adopted October 2011) and Policy DM6 of the Development Management Policies Local Development Document (adopted July 2013).  National Planning Policy requires Local Authorities to ensure that a protected species survey is undertaken for applications that may be affected prior to determination of a planning application.

7.8.3	The application has been submitted with a Biodiversity Checklist and accompanying Report which concludes that the site is considered to be of low ecological value.  The submitted details have been reviewed by Hertfordshire Ecology who concur with the findings but note that there is some potential for nesting birds to use the trees and scrub on the adjacent site.  Bats may also be using the adjacent woodland for foraging and commuting.

7.8.4	A condition on any grant of consent would prevent the removal of trees, hedges or scrub between 1 March and 31 August inclusive unless searched immediately beforehand and certified free of nesting birds by a qualified ecologist.  A condition would also be attached to require the submission of details of any external lighting.  An advisory informative regarding bats is also suggested.  The submitted ecology report also includes ecological enhancements which should be incorporated into the proposed development.

7.9	Sustainability

7.9.1	Paragraph 93 of the NPPF states that:

“Planning plays a key role in helping to shape places to secure radical reductions in greenhouse gas emissions, minimising vulnerability and providing resilience to the impacts of climate change, and supporting the delivery of renewable and low carbon energy and associated infrastructure”.

7.9.2	Policy CP1 of the Core Strategy requires the submission of an Energy and Sustainability Statement demonstrating the extent to which sustainability principles have been incorporated into the location, design, construction and future use of proposals and the expected carbon emissions.

7.9.3	Policy DM4 of the Development Management Policies requires applicants to demonstrate that development will produce 5% less carbon dioxide emissions than Building Regulations Part L (2013) requirements having regard to feasibility and viability. This may be achieved through a combination of energy efficiency measures, incorporation of on-site low carbon and renewable technologies, connection to a local, decentralised, renewable or low carbon energy supply. The policy states that from 2016, applicants will be required to demonstrate that new residential development will be zero carbon. However, the Government has announced that it is not pursuing zero carbon and the standard remains that development should produce 5% less carbon dioxide emissions than Building Regulations Part L (2013) requirements having regard to feasibility and viability.

7.9.4	The submitted Energy Report identifies that the proposed development would be compliant with Policy DM4 and would provide 5% less carbon emissions than Building Regulations through the provision of solar panels along the building.  Any permission would include a condition requiring the siting of the solar panels to be submitted.

7.10	Refuse & Recycling

7.10.1	Policy DM10 (Waste Management) of the Development Management Policies LDD (adopted July 2013) advises that the Council will ensure that there is adequate provision for the storage and recycling of waste and that these facilities are fully integrated into design proposals.  New developments will only be supported where:

i) The siting or design of waste/recycling areas would not result in any adverse impact to residential or work place amenity

ii) Waste/recycling areas can be easily accessed (and moved) by occupiers and by local authority/private waste providers

iii) There would be no obstruction of pedestrian, cyclists or driver site lines

7.10.2	The submitted plans indicate a communal refuse area adjacent to the proposed parking area with a maximum length of 3.7 metres and depth of 1.9 metres.  The refuse area would be enclosed by 1.7 metre high natural timber cladding.  Environmental Protection have confirmed verbally that the area would be of sufficient size for the number of units proposed and the Highways Officer makes reference to the refuse area being sited an acceptable distance from the highway to enable collection.

7.10.3	The bin store would be sited adjacent to the boundary with No. 30 Ashridge Drive, however, there is existing fencing along the boundary and this dwelling is set off the boundary with a detached garage sited between it and application site boundary.  As such it is not considered that the relationship would be unacceptable.

7.11	Safety & Security

7.11.1	Policy CP1 of the Core Strategy (adopted October 2011) advises that all development in Three Rivers will contribute to the sustainability of the District.  This means taking into account the need to, for example, promote buildings and public spaces that reduce opportunities for crime and anti-social behaviour. Policy CP12 also requires that development proposals design out opportunities for crime and anti-social behaviour through the incorporation of appropriate measures to minimise the risk of crime and create safe and attractive places.

7.11.2	It is suggested that a management plan providing details of the long term management and maintenance of the building be provided by condition.

7.11.3	Any planning permission would include an informative to ensure that the development is built to Secured by Design part 2, the police approved minimum security standard.  This would ensure, for example, that exterior doors and windows are of appropriate standard.

7.12	Infrastructure Provision

7.12.1	Policies CP8 and CP10 of the Core Strategy (adopted October 2011) require development to make adequate contribution to infrastructure and services.  The Community Infrastructure Levy (CIL) is a planning charge, introduced by the Planning Act 2008 as a tool for local authorities in England and Wales to help deliver infrastructure to support the development of their area. It came into effect In Three Rivers on 1 April 2015 following the adoption by the Council of the CIL Charging Schedule in February 2015. The application site is located within Area C which has a CIL rate of £Nil.

7.13	Other Matters

7.13.1	The development would be required to comply with relevant Building Regulations including in relation to the provision of fire hydrants.

7.14	Conclusion

7.14.1	Whilst some individual elements of the proposal, taken in isolation, may not fully accord with TRDC policy or standards, the proposal requires assessment as a whole.  Any shortfalls must be viewed in this context and with regard to the specific circumstances of the application site.  It is considered that the proposed development would not result in any demonstrable harm to the character of the area and an acceptable relationship would be maintained between the proposed development and existing residential properties.  There is an identified need for affordable housing for the homeless within the District and the proposal will help meet this need.

8.	Recommendation

8.1	That PLANNING PERMISSION BE GRANTED, subject to the following conditions:

C1	Time

The development hereby permitted shall be begun before the expiration of three years from the date of this permission.

Reason: In pursuance of Section 91(1) of the Town and Country Planning Act 1990 and as amended by the Planning and Compulsory Purchase Act 2004.

C2	Plans

The development hereby permitted shall be carried out in accordance with the following approved plans: 010 A; 020 B; 022 B; 100 A; 101 B; 103 B; 110 B; 200 D; 201 B; 210 C; 400; 700 A; 701 A.

Reason: For the avoidance of doubt, in the proper interests of planning and to safeguard the character and appearance of the Conservation Area and amenity of neighbouring occupiers; in accordance with Policies PSP2, CP1, CP2, CP3, CP4, CP6, CP8, CP9, CP10 and CP12 of the Core Strategy (adopted October 2011) and Policies DM1, DM4, DM6, DM8, DM9, DM10, DM11, DM12, DM13 and Appendices 2 and 5 of the Development Management Policies LDD (adopted July 2013).

C3	Materials

Before any building operations above ground level hereby permitted are commenced, samples and details of the proposed external materials shall be submitted to and approved in writing by the Local Planning Authority and no external materials shall be used other than those approved.

Reason: To prevent the building being constructed in inappropriate materials in accordance with Policies CP1 and CP12 of the Core Strategy (adopted October 2011) and Policy DM1 and Appendix 2 of the Development Management Policies LDD (adopted July 2013).

C4	Parking / Access – Details

Prior to the commencement of the development hereby permitted full details (in the form of scaled plans) shall be submitted in relation to the proposed parking / access area to demonstrate the following:

- Swept Path analysis for vehicles using the site.

Reason: This is a pre commencement condition in the interest of highway safety and traffic movement and to meet the requirements of Policies CP1 and CP10 of the Core Strategy (adopted October 2011).

C5		Construction Management Plan (CMP)

The development shall not begin until full details of all proposed construction vehicle access, movements, parking arrangements and wheel washing facilities have been submitted to and approved in writing by the Local Planning Authority. The relevant details should be submitted in the form of a Construction Management Plan and the approved details are to be implemented throughout the construction programme.

Reason: This is a pre commencement condition to minimise danger, obstruction and inconvenience to users of the highway in accordance with Policies CP1 and CP10 of the Core Strategy (adopted October 2011) and Policy DM13 and Appendix 5 of the Development Management Policies LDD (adopted July 2013).

C6		Landscaping - Details

No development shall take place until there has been submitted to and approved in writing by the Local Planning Authority a scheme of hard and soft landscaping, which shall include the location of all existing trees and hedgerows affected by the proposed development, and details of those to be retained, together with a scheme detailing measures for their protection in the course of development.

All hard landscaping works required by the approved scheme shall be carried out and completed prior to the first occupation of the development hereby permitted. All soft landscaping works required by the approved scheme shall be carried out in accordance with a programme to be agreed before development commences and shall be maintained including the replacement of any trees or plants which die are removed or become seriously damaged or diseased in the next planting season with others of a similar size or species, unless the Local Planning Authority gives written consent to any variation for a period for five years from the date of the approved scheme was completed.

Reason: This is a pre commencement condition in the interests of visual amenity in accordance with Policies CP1 and CP12 of the Core Strategy (adopted October 2011) and Policy DM6 of the Development Management Policies LDD (adopted July 2013).

C7	Tree Protection Scheme – Details

No operations (including tree felling, pruning, demolition works, soil moving, temporary access construction, or any other operation involving the use of motorised vehicles or construction machinery) shall commence on site in connection with the development hereby approved until the branch structure and trunks of all trees shown to be retained and all other trees not indicated as to be removed and their root systems have been protected from any damage during site works, in accordance with a scheme to be submitted to and approved in writing by the Local Planning Authority.

The protective measures, including fencing, shall be undertaken in accordance with the approved scheme before any equipment, machinery or materials are brought on to the site for the purposes of development, and shall be maintained until all equipment, machinery and surplus materials have been removed from the site.  Nothing shall be stored or placed within any area fenced in accordance with this condition and the ground levels within those areas shall not be altered, nor shall any excavation be made, without the written consent of the Local Planning Authority. No fires shall be lit or liquids disposed of within 10.0m of an area designated as being fenced off or otherwise protected in the approved scheme.

Reason: This is a pre commencement condition to protect the visual amenities of the trees, area and to meet the requirements of Policies CP1 and CP12 of the Core Strategy (adopted October 2011) and Policy DM6 of the Development Management Policies LDD (adopted July 2013).

C8	Arboricultural Method Statement

No development or other operation shall commence on site until a scheme (herein called the Approved Method Statement of Arboricultural Works Scheme) which indicates the construction methods to be used in order to ensure the retention and protection of tree, shrubs and hedges growing on or adjacent to the site has been submitted to and approved in writing by the local planning authority.

No operations shall commence on site in connection with the development hereby approved (including tree felling, pruning, demolition works, soil moving, temporary access construction, or any other operation involving the use of motorised vehicles or construction machinery) until the tree protection works required by the approved scheme are in place on site.

The fencing or other works which are part of the approved scheme shall not be moved or removed, temporarily or otherwise, until all works including external works have been completed and all equipment, machinery and surplus materials removed from the site, unless the prior approval of the local planning authority has first been sought and obtained.

Reason: This is a pre commencement condition to ensure that the protected trees are not affected during construction of the development hereby permitted, in the interests of visual amenity and in accordance with Policies CP1 and CP12 of the Core Strategy (adopted October 2011) and Policy DM6 of the Development Management Policies LDD (adopted July 2013).

C9	Housing Details

The accommodation hereby permitted shall only be occupied by persons that have an open homeless application with the Local Authority.

Reason: To meet local housing need within the Three Rivers district and to comply with Policies CP1, CP2, CP3 and CP4 of the Core Strategy (adopted October 2011).

C10	Management & Maintenance Plan – Details

Prior to occupation of the development hereby permitted, an Operational Management Plan including details of how the development would be effectively managed shall be submitted to and approved in writing by the Local Planning Authority.  The Operational Management Plan should include details of the operation and management of the refuse storage area and general site maintenance.  The development shall be operated and managed in accordance with the approved Operational Management Plan.

Reason: In the interests of the local environment and residential amenity in accordance with Policies CP1, CP9 and CP12 of the Core Strategy (adopted October 2011) and Policies DM1, DM6, DM9, DM10 and Appendix 2 of the Development Management Policies LDD (adopted July 2013).

C11	Sustainability – Details

Prior to the commencement of development hereby permitted, plans and details of the solar panels shall be submitted to and approved in writing by the Local Planning Authority. The approved details and energy saving measures detailed within the submitted Energy Statement shall be implemented prior to occupation of the development and permanently maintained thereafter.

Reason: This condition is a pre commencement condition to ensure that the development meets the requirements of Policy CP1 of the Core Strategy (adopted October 2011) and Policy DM4 of the Development Management Policies LDD (adopted July 2013) and to ensure that the development makes as full a contribution to sustainable development as possible.

C12	Nesting Season

No removal of trees, hedges or scrub shall take place between 1 March and 31 August inclusive unless searched immediately beforehand and certified free of nesting birds by a qualified ecologist.

Reason: To protect the amenities of wildlife during the primary nesting season and to meet the requirements of Policies CP1 and CP9 of the Core Strategy (adopted October 2011) and Policy DM6 of the Development Management Policies LDD (adopted July 2013).

C13	Lighting – Details

No external lighting shall be installed on the site or affixed to any buildings on the site unless the Local Planning Authority has first approved in writing details of the position, height, design and intensity. The lighting shall be installed in accordance with the approved details before the use commences.

Reason: In the interests of visual amenity and biodiversity and to meet the requirements of Policies CP1, CP9 and CP12 of the Core Strategy (adopted October 2011) and Policies DM6 and DM9 of the Development Management Policies LDD (adopted July 2013).

C14		Ecological Enhancements

The development shall be carried out in accordance with the recommendations set out at section 5.1 of the Ecological Appraisal (September 2017) submitted and approved as part of this application.

Reason: In the interests of biodiversity and to meet the requirements of Policies CP1, CP9 and CP12 of the Core Strategy (adopted October 2011) and Policies DM6 and DM9 of the Development Management Policies LDD (adopted July 2013).

C15	Refuse & Recycling – Implementation

The development hereby permitted shall not be occupied until the approved scheme as shown on plan no. 400 (Bin Storage) has been implemented and these facilities should be retained permanently thereafter.

Reason: To ensure that satisfactory provision is made, in the interests of amenity and to ensure that the visual appearance of such provision is satisfactory in compliance with Policies CP1 and CP12 of the Core Strategy (adopted October 2011) and Policies DM1, DM3, DM10 and Appendix 2 of the Development Management Policies document (adopted July 2013).

C16	Details of Boundary Treatment

Prior to occupation of the development hereby permitted, a plan indicating the positions, design, materials and type of boundary treatment to be erected on the site shall be submitted to and approved in writing by the Local Planning Authority. The boundary treatment shall be erected prior to occupation in accordance with the approved details and shall be permanently maintained as such thereafter.

Reason: To ensure that appropriate boundary treatments are proposed to safeguard the amenities of neighbouring properties and the character of the locality in accordance with Policies CP1 and CP12 of the Core Strategy (adopted October 2011) and Policy DM1 and Appendix 2 of the Development Management Policies LDD (adopted July 2013).

C17	Parking Management Plan

A parking management plan, including details of the allocation and management of vehicle parking spaces and cycle storage spaces within the development; and long term management responsibilities and maintenance schedules for the parking area, shall be submitted to and approved in writing by the Local Planning Authority prior to the first occupation of the development hereby approved. The parking management plan shall be carried out in accordance with the approved details.

Reason: To ensure that adequate off-street parking and manoeuvring space is provided within the development so as not to prejudice the free flow of traffic and in the interests of highway safety on neighbouring highways in accordance with Policies CP1, CP10 and CP12 of the Core Strategy (adopted October 2011) and Policy DM13 and Appendix 5 of the Development Management Policies LDD (adopted July 2013).

C18	Fire Hydrant Provision

Should they be required, detailed proposals for fire hydrants serving the development as incorporated into the provision of the mains water services for the development, whether by means of existing water services or new mains or extension to or diversion of existing services or apparatus, shall be submitted to and approved in writing by the Local Planning Authority prior to the occupation of development. The development shall thereafter be implemented in accordance with the approved details prior to occupation of any building forming part of the development.

Reason: To ensure that there is adequate capacity for fire hydrants to be provided and to meet the requirements of Policies CP1 and CP8 of the Core Strategy (adopted October 2011).

C19		Obscure Glazing

Before the first occupation of the building/extension hereby permitted the window(s) as shown on plans 200 D and 201 B, as being translucent windows, including the oriel windows, shall be fitted with purpose made obscured glazing to a height of 1.7m above the floor level of the room of the in which the window is installed and shall be top level opening only at 1.7m above the floor level of the room in which the window is installed. The window(s) shall be permanently retained in that condition thereafter.

Reason: To safeguard the amenities of the occupiers of neighbouring residential properties in accordance with Policies CP1 and CP12 of the Core Strategy (adopted October 2011) and Policy DM1 and Appendix 2 of the Development Management Policies LDD (adopted July 2013).

C20	Bollards

No part of the development hereby permitted shall be first occupied until the proposed timber bollards (shown on drawing no. 022 B) have been constructed.  The bollards shall be permanently maintained as such thereafter.

Reason: In the interests of visual amenity and the character and appearance of the area in accordance with Polices CP1 and CP12 of the Core Strategy (adopted October 2011).

8.2	Informatives:

I1	With regard to implementing this permission, the applicant is advised as follows:

All relevant planning conditions must be discharged prior to the commencement of work. Requests to discharge conditions must be made by formal application. Fees are £116 per request (or £34 where the related permission is for extending or altering a dwellinghouse or other development in the curtilage of a dwellinghouse). Please note that requests made without the appropriate fee will be returned unanswered.

There may be a requirement for the approved development to comply with the Building Regulations. Please contact Hertfordshire Building Control (HBC) on 0208 207 7456 or at buildingcontrol@hertfordshirebc.co.uk who will be happy to advise you on building control matters and will protect your interests throughout your build project by leading the compliance process. Further information is available at www.hertfordshirebc.co.uk.

Community Infrastructure Levy (CIL) - If your development is liable for CIL payments, it is a requirement under Regulation 67 (1) of The Community Infrastructure Levy Regulations 2010 (As Amended) that a Commencement Notice (Form 6) is submitted to Three Rivers District Council as the Collecting Authority no later than the day before the day on which the chargeable development is to be commenced. DO NOT start your development until the Council has acknowledged receipt of the Commencement Notice. Failure to do so will mean you will lose the right to payment by instalments (where applicable), lose any exemptions already granted, and a surcharge will be imposed.

Care  should  be  taken  during  the  building  works  hereby  approved  to  ensure  no  damage occurs to the verge or footpaths during construction. Vehicles delivering materials to this development shall not override or cause damage to the public footway. Any damage will require to be made good to the satisfaction of the Council and at the applicant's expense.

Where possible, energy saving and water harvesting measures should be incorporated. Any external changes to the building which may be subsequently required should be discussed with the Council's Development Management Section prior to the commencement of work.

I2	The applicant is reminded that the Control of Pollution Act 1974 allows local authorities to restrict construction activity (where work is audible at the site boundary). In Three Rivers such work audible at the site boundary, including deliveries to the site and running of equipment such as generators, should be restricted to 0800 to 1800 Monday to Friday, 0900 to 1300 on Saturdays and not at all on Sundays and Bank Holidays.

I3	The Local Planning Authority has been positive and proactive in its consideration of this planning application, in line with the requirements of the National Planning Policy Framework and in accordance with the Town and Country Planning (Development Management Procedure) (England) Order 2015. The scheme has been amended following the withdrawal of a previous application, resulting in a form of development that maintains/improves the economic, social and environmental conditions of the District.

I4	Storage of materials: The applicant is advised that the storage of materials associated with the construction of this development should be provided within the site on land which is not public highway, and the use of such areas must not interfere with the public highway. If this is not possible, authorisation should be sought from the Highway Authority before construction works commence. Further information is available via the website https://www.hertfordshire.gov.uk/services/highways-roads-and-pavements/highways-roads-and-pavements.aspx or by telephoning 0300 1234047.

I5	Secured By Design: The applicant encouraged to construct the development to the standards of Secured by Design part 2, which is the police approved minimum security standard and also achieves ADQ (Building Regulation regarding security).

I6	Bats: Bats are protected under domestic and European legislation where, in summary, it is an offence to deliberately capture, injure or kill a bat, intentionally or recklessly disturb a bat in a roost or deliberately disturb a bat in a way that would impair its ability to survive, breed or rear young, hibernate or migrate, or significantly affect its local distribution or abundance; damage or destroy a bat roost; possess or advertise/sell/exchange a bat; and intentionally or recklessly obstruct access to a bat roost.

If bats are found all works must stop immediately and advice sought as to how to proceed from either of the following organisations:

The UK Bat Helpline: 0845 1300 228

Natural England: 0300 060 3900

Herts & Middlesex Bat Group: www.hmbg.org.uk

or an appropriately qualified and experienced ecologist.

(As an alternative to proceeding with caution, the applicant may wish to commission an ecological consultant before works start to determine whether or not bats are present. A list of bat consultants can be obtained from Hertfordshire Ecology on 01992 555220).